## Slide 1
X-Ray–Guided Robotic Catheter Intervention
Simulation Workflow — Release Status & Roadmap
▸ Cosserat rod XPBD physics (Newton upstream + vessel-mesh collision)
▸ Slang GPU Beer-Lambert DRR renderer (inline catheter compositing)
▸ Unified sim loop (physics → render → RL obs, zero CPU sync on hot path)
▸ Interactive UI demo + RL training pipeline (RSL-RL PPO, 512 envs)
Isaac for Healthcare | May 2026

## Slide 2
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Architecture Overview — Four-Stage Pipeline
Stage 1 CT Ingestion
CT/CTA → HU→μ conversion → 3D μ-volume Vessel segmentation → wp.Mesh (collision) Centerline (VMTK) → Dijkstra arrival map
Stage 2 Sim Environment
XCathRodSolver (XPBD + vessel-mesh SDF) Slang DRR renderer (Beer-Lambert, inline catheter) Unified loop: physics → render → RL obs
Stage 3 RL Training
RSL-RL PPO | 512 parallel envs State obs today → Pixel obs Sprint 2 GR00T-N IL + RL fine-tune
Stage 4 Deployment
Holoscan IGX | <10 ms inference XCath robotic catheter | Safety layer Sim-to-real via domain randomization
▶
▶
▶
All four stages share one coordinate frame (CT-volume mm). The same μ-volume fed to the renderer is derived from the same CT as the collision mesh — physics and imaging are always registered to the same patient anatomy.

## Slide 3
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Unified Sim Loop — Per-Timestep Execution
Five GPU-resident steps per frame. No CPU↔GPU synchronization on the hot path.
Step 1
Root Control
Proximal boundary condition updated via GPU kernel. Insertion depth δ and rotation angle θ written directly to the proximal particle position + orientation buffers. Warp kernels: apply_proximal_control_gpu / set_root_orientation Both are CUDA-graph capturable — zero CPU sync.
Step 2
Physics Step (XPBD CUDA graph)
CUDA graph replayed — entire N-substep loop fires as one graph node. Each substep: predict → assemble JMJT → block-Thomas direct solve → apply Δx → integrate. Vessel-mesh SDF + AABB collision constraints applied before/after solve. 1,300 Hz throughput per environment. Scales to 512 envs via flat buffer offsets.
Step 3
Segment Buffer Update
Particle positions (N×3 float32, GPU-resident) written to the renderer's CatheterSegmentData buffer (N×8 floats: xyz0, xyz1, radius, μ). No host transfer. No CT volume modification.
Step 4
Render Call (Slang DRR)
Ray-march kernel dispatched over H×W detector grid. CT μ-volume is a static GPU texture — never reloaded per frame. Catheter composited inline: μ_total(s) = μ_CT(s) + Σᵢ μᵢ · √(1−dᵢ²/rᵢ²) Realism pipeline: Poisson noise → PSF → gamma → misregistration jitter.
Step 5
Output
Fluoroscopy frame (H×W float32, GPU tensor) → RL policy input. Catheter state vector (tip xyz, orientation, insertion depth) → reward. Both outputs GPU-resident. No host round-trip.
Why this is fast: CT volume never moves. Only the N×8 catheter buffer changes per frame. CUDA graph eliminates physics launch overhead. ~63 FPS @ 256² / ~25 FPS @ 512² (A6000).

## Slide 4
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Newton Upstream Algorithms — Ported to Isaac Lab
XPBDRodSolver is a faithful port of Newton's SolverXPBDRod (PR #1981). Feature parity maintained — research advances in Newton propagate directly into the Isaac Lab training environment.
Core Algorithms Upstreamed
Block-Thomas Direct Solve
Tridiagonal block factorization for the XPBD constraint system. Linear in rod length O(N). Numerically stable for stiff Cosserat rods. Runs entirely on GPU — no LAPACK, no CPU fallback.
Split-Thomas Solve
Decoupled positional and rotational Thomas passes. Alternative backend selectable via XPBD_DIRECT_SOLVE_SPLIT_THOMAS.
Block-Jacobi Solve
Parallel block-diagonal approximation. Lower memory bandwidth. Useful when block-Thomas bandwidth is the bottleneck at very high N.
Banded Cholesky Solve
Half-bandwidth KD=11, leading dimension LDAB=34. Exact Cholesky for small dense systems (N_dof ≤ 64).
Tiled Cholesky (GPU tile)
wp.tile_load for small dense systems — fits in shared memory tile. Avoids global memory round-trip for <64-DOF sub-problems.
Floor Collision
Configurable restitution coefficient (0–1). Applied as a position correction constraint — parity with Newton upstream.
Vessel-Mesh Collision (XCathRodSolver)
SDF Containment (wp.mesh_query_point_sign_normal)
BVH query per particle. Signed distance to nearest surface point. Particles outside vessel lumen projected back along surface normal. sign_scale=1.0, target_phi=−0.001 m (1 mm inside wall).
AABB Broadphase (wp.mesh_query_aabb)
Rod-segment bounding box queried against mesh triangle AABB tree. Candidate triangle faces → vertex-triangle + rod-segment-to-edge contacts. collision_iterations=2 per substep.
Track-Guided Insertion
Non-tip particles projected to linear insertion axis. track_start + track_dir + track_length define the sheath entry axis. tip_num_edges controls how many distal segments are free to deflect.
Constraint Hooks
_pre_constraints_hook: vessel SDF applied before XPBD stretch/bend. _post_constraints_hook: AABB edge contacts applied after XPBD solve. Extensible — additional constraint classes can be injected here.
CUDA-Graph Compatible
All collision kernels are Warp kernels captured inside the same CUDA graph as the XPBD substep loop. Zero CPU sync per substep.

## Slide 5
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Multi-Environment Batched Physics — 512 Parallel Rods
All N environments dispatched in a single Warp kernel launch and a single CUDA graph replay. No per-environment CPU synchronization.
How Batching Works
_BatchedWorkspace allocates flat contiguous GPU buffers: positions[total_particles × 3], orientations[total_particles × 4].
rod_offsets[r] and edge_offsets[r] give each environment's slice — one kernel launch processes all rods in parallel without branching.
CUDA-graph capture covers the entire multi-environment substep loop. wp.ScopedCapture on first step() call; wp.capture_launch on all subsequent calls.
GPU-side proximal control: apply_proximal_control_gpu and set_root_orientation are Warp kernels — safe to capture inside the CUDA graph, zero CPU sync on hot path.
Memory cost scales linearly with N (particle count × envs). Compute cost is dominated by the block-Thomas solve — nearly O(N×envs) with the flat buffer layout.
Batched Rendering
renderDRR_forward_batched: single Slang dispatch. dispatchThreadID.z indexes the environment.
Per-environment catheter geometry packed into a flat StructuredBuffer<CatheterSegment> with per-env offset + count indices — different catheter per env, single kernel.
L2 cache bottleneck at N>8: shared 3D μ-volume exceeds L2 capacity. Sprint 2 fix: Texture2DArray caches one depth slice per env in L2.
Performance (NVIDIA A6000)
Component
Throughput
Status
Physics — 1 env
1,300 Hz
✓ Target met
Physics — 512 envs
~60 Hz
✓ Target met
Render — 256² 1 env
~263 FPS
Interactive demo
Render — 512² 1 env
~25 FPS
Standalone bench
Render — 512² N≤4
~25 FPS
Production today
Render — 512² N=8+
Degrades
Sprint 2 fix
Full loop (256²)
~63 FPS
Physics+render

## Slide 6
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Fluoroscopy Rendering — Compositing Paths
Slang GPU (unified loop)
~63 FPS @ 256×256 ~25 FPS @ 512×512 (NVIDIA A6000)
Fused volume + catheter Beer-Lambert in single GPU ray march. Catheter composited inline: μ_total(s) = μ_CT(s) + Σᵢ μᵢ·√(1−dᵢ²/rᵢ²) Static CT μ-volume on GPU texture. Only catheter segment buffer changes per frame. Post-processing on same GPU timeline: Poisson → PSF → gamma → jitter.
CPU Beer-Lambert (reference path)
~2–5 FPS (NumPy, CPU) Reference only
NumPy ray-march for offline ground-truth generation and renderer validation. Per-segment cylinder chord: t(d) = 2·√(r²−d²) for d<r, else 0. Final: I = I₀·exp(−Σᵢ μᵢ·chord_norm(u,v)) Post-processing: scatter convolution → Poisson → PSF → gamma (realism.py, CPU NumPy). NOT on the RL training path — for validation and visual QA only.
Isaac Lab USD quad (planned — Sprint 2)
Real-time (RTX) Planned Sprint 2
DRR backdrop texture applied to a 3D USD quad in Omniverse viewport. Capsule prims for catheter markers. RTX path tracing for photoreal scatter. Intended for visual QA and demo purposes — not for RL training data.
Key property: Catheter attenuation is additive in the exponent — μ_total = μ_CT + μ_catheter — so the catheter attenuates rather than occludes. Self-crossings produce physically correct increased opacity. Background anatomy remains visible through the catheter wire (exp(−μ) < 1, > 0).

## Slide 7
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Beer-Lambert Catheter Compositing — Algorithm Detail
Per-sample-point inline compositing inside the GPU ray march. Same Beer-Lambert integral for CT and catheter — no separate compositing pass.
1
DRR Background
Ray march through 3D CT μ-volume (GPU texture, static per patient). Fixed-step integration: I_DRR = I₀·exp(−∫μ_CT(s) ds) HU→μ piecewise linear map. Dense bone ~0.3–0.5 mm⁻¹. Air ~0.0 mm⁻¹.
2
Catheter Segment Buffer
Physics particle positions (N×3 float32) written to GPU segment buffer. Each segment: (xyz_proximal, xyz_distal, radius, μ) — 8 floats. Per-segment μ profile: tungsten marker 3.0, NiTi shaft 0.8, polymer tip 0.15, Pt marker 5.0.
3
Inline Perpendicular Test
At each ray sample point s, for each catheter segment i: d_i = perpendicular distance from s to segment axis if d_i < r_i: contribute μᵢ·√(1−dᵢ²/rᵢ²) to running integral The √(1−d²/r²) factor is a chord-length weight — exact for a circular cross-section.
4
Fused Integral
μ_total(s) = μ_CT(s) + Σᵢ μᵢ·√(1−dᵢ²/rᵢ²) I_final = I₀·exp(−∫μ_total(s) ds) Catheter and CT share one exponent — no separate compositing pass, no alpha blending.
5
Detector Realism
Poisson quantum noise (photon count N_ph → Poisson(N_ph·I)) PSF convolution (Gaussian σ=0.7 px — scintillator light spread) Gamma correction + misregistration jitter (σ_rot=0.05°, σ_trans=0.1 mm)

## Slide 8
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Stage 1 — CT Ingestion Pipeline
Runs once per patient anatomy. Produces two GPU-resident assets that every downstream stage depends on.
CT / CTA Input (DICOM / NIfTI)
Raw 3D Hounsfield Unit volume from clinical scanner.
HU → μ Conversion
Piecewise-linear map: HU[−1000,3000] → μ[0, 0.5] mm⁻¹. Dense bone ~0.3–0.5. Soft tissue ~0.02–0.05. Air ~0.0.
μ Volume (3D tensor)
Uploaded to GPU texture once. Static for entire training session. → Fed to Slang DRR renderer every frame.
Vessel Segmentation
HU threshold on contrast-enhanced CT (vessels ~100–300 HU above baseline). → Binary vessel mask.
Mesh Generation
Marching Cubes / VTK on binary mask → polygon mesh. Converted to warp.Mesh (metres). → Collision geometry for XCathRodSolver.
Centerline Extraction
VMTK centerline skeleton from vessel mask. → CenterlineGraph (nodes + edges). → Dijkstra arrival map for temporal bolus dynamics.
Key: The CT volume is a static 3D texture on the GPU. Only the catheter geometry buffer changes frame-to-frame. This is why the renderer can run at 25–63 FPS — no per-frame CT reconstruction.

## Slide 9
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
DSA Pipeline + Temporal Bolus Dynamics
4-step Digital Subtraction Angiography. Gamma-variate contrast kinetics + Dijkstra arrival map.
1. Mask DRR
Render anatomy without contrast (before injection). C-arm pose recorded precisely.
▶
2. Contrast DRR
Inject bolus: Δμ(v,t) = μ_iodine · C(t − T(v)) · vessel_mask(v) C(t): gamma-variate c_peak·(t/t_peak)^α·exp(α(1−t/t_peak)) T(v): per-voxel arrival time from Dijkstra on CenterlineGraph.
▶
3. Scatter + Jitter
apply_scatter() adds Compton scatter haze. apply_misregistration(): σ_rot=0.05°, σ_trans=0.1 mm — simulates patient motion. Critical: introduces bone-edge residuals that monoenergetic rendering suppresses.
▶
4. Subtract + Post
DSA = contrast_DRR − mask_DRR (in log domain). Post-process: normalize → gamma → clip → vessel boost (μ×factor on mask).
XCath Bolus Validation Results (not yet merged into fluorosim)
XCath validated Hagen-Poiseuille (power=2.0) and Feeding Trunk Excision (F-8) against real clinical DSA. These results are algorithmically proven but the code changes are not yet merged into the fluorosim repo. Current fluorosim uses Dijkstra with simple edge weights and multi-root injection. Merge target: Sprint 2.
Metric
Current fluorosim
XCath validated (not merged)
Real DSA
Bolus delay
Not calibrated
1.90 s (Hagen-Poiseuille)
2.13 s
Peak delay error
—
11% (was 2.6×)
—
Distal MCA vel.
Not modelled
25% ICA (viscous resist.)
Realistic
Injection coverage
All roots
43.1% (F-8 selective)
ICA territory

## Slide 10
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Performance Baseline (NVIDIA A6000)
Physics is solved. Rendering is the diagnosed remaining constraint with a clear engineering path.
Component
Resolution / Scale
Throughput
Target
Status
Single-env physics (XPBD)
20-seg rod
1,300 Hz
>1,000 Hz
✓ Met
Multi-env physics
512 envs
~60 Hz
>60 Hz
✓ Met
GPU DRR + catheter (fused)
256×256 1 env
~263 FPS
<5 ms
✓ Met
GPU DRR + catheter (fused)
512×512 1 env
~25 FPS
<5 ms
In Progress
GPU DRR batched
512×512 N≤4
~25 FPS
>60 Hz
In Progress
GPU DRR batched
512×512 N>8
Degrades
>60 Hz
Sprint 2
CPU Beer-Lambert
512×512 ref.
2–5 FPS
N/A
Reference only
Full sim loop (interact.)
256×256 1 env
~63 FPS
30+ FPS
✓ Met
Sprint 2 bottleneck fix: 3D μ-volume → Texture2DArray — caches one depth slice per env in L2. Eliminates global memory bandwidth saturation at N>8. Projected throughput: >60 Hz @ 512 envs.
Physics subsystem exceeds training throughput target with margin. End-to-end loop is rendering-bound only. No unknown unknowns on this slide.

## Slide 11
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
RL Training Pipeline — State-Based (Sprint 1)
PPO via RSL-RL. 512 parallel environments. State observations today → pixel observations Sprint 2.
Environment
Multi-env production XPBD solver with gymnasium-compatible step/reset interface. Two control actions: advance (proximal push) + rotate — matching real procedure DOF. Reward: reduction in tip-to-target Euclidean distance. Dense, well-conditioned.
RSL-RL Wrapper
Standard VecEnv adapter. RL algorithm fully decoupled from physics/rendering. Swapping to pixel obs or a different policy algorithm requires only obs tensor shape change.
PPO Config
Hyperparameters tuned for catheter navigation: higher entropy (exploration at bifurcations), shorter GAE horizon (reduce variance from contact sequences).
Training Scale
512 parallel environments. Policy sees 512 independent rollout trajectories per update. Physics runs at ~1,300 Hz/env inside a single CUDA graph — RL training is not physics-bound. Currently rendering-bound only if pixel obs are enabled.
Smoke Test
Dependency-free validation path: reset → step → reward → done, no RSL-RL stack required. CI validation + headless server debugging without full training stack.
State-based observations are scaffolding, not the target. Sprint 2: pixel obs from Slang renderer → policy navigates using only the fluoroscopy frame — closing the loop from simulation to deployable clinical AI.

## Slide 12
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Stage 1 & 2 Demo — Interactive Fluoroscopy Simulator
Browser-based UI integrating XPBD physics, Beer-Lambert rendering, vessel-mesh collision, and DSA in real time.
Control Panel
• C-arm projection: AP / LAO-30 / LAO-45 / RAO-30 / Lateral (instant re-render)
• Advance speed (mm/s) slider → proximal boundary condition in XPBD solver
• Advance / Retract: 3 physics substeps per click
• Rotate CW / CCW: proximal torque, propagates along Cosserat rod
• Idle step: physics advance with zero control (gravity deformation)
• Reset: restore to initial straight configuration via Warp buffer write + CUDA graph invalidation
• DSA: 3-dispatch composite (bg + fat-catheter + catheter)
Simulation Info (live)
• Projection: current C-arm angle
• Tip (CT mm): catheter tip in CT volume coordinates
• Catheter bend (mm): max deviation from straight line — confirms vessel collision is active
• Physics step: substep time (ms)
• Render (GPU): DRR dispatch time (ms)
• Sim loop: total frame time + FPS
Why Interactive Instead of PPO Rollout
Claim
Why a pre-recorded rollout cannot prove it
Physics runs at interactive speed
A recording can be played at any speed
Vessel collision is active
A scripted trajectory can be collision-free by design
DRR re-renders at correct C-arm angle
Policy rollouts typically use a fixed angle
DSA + fluoro are spatially registered
Hard to verify in a pre-rendered sequence
Full pipeline runs in ~12 ms
A video says nothing about throughput
Launch: conda activate isaaclab → python3 interactive_catheter_fluoro.py --ct-dir /tmp/patient_001 --share

## Slide 13
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
XCath Collaboration — Technical Outcomes
5 algorithmic improvements validated against real clinical DSA data. XCath embedded in the sprint — weekly technical sync with Jung-eun Park (AI/ML, XCATH Robotics).
Implemented in fluorosim
Validated by XCath — not yet merged
Analysis result — no code change
1. Hagen-Poiseuille Blood Flow Model
Validated — not merged
Murray's Law (power=0.5) → Hagen-Poiseuille (power=2.0) Bolus delay: 5.6s → 1.90s sim vs 2.13s real (89% match, was 2.6× off) Distal MCA velocity: 71% ICA → 25% ICA (viscous resistance) Not in fluorosim codebase — algorithm designed & validated by XCath on their data. Merge target: Sprint 2.
2. Selective Injection (Feeding Trunk Excision F-8)
Validated — not merged
Voronoi partition on centerline graph + excise non-selected trunks. Single-root coverage: 43.1% nodes — matches real ICA territory. Peak delay: 2.20s sim vs 2.13s real (3% error) Not in fluorosim codebase — designed & validated by XCath. Merge target: Sprint 2.
3. Dispersion Correction
Validated — not merged
β_eff = β₀ + k·arrival_time (k=0.15) — FWHM widening. β_eff += α_res / max(r_voxel, 0.1) — thin vessels wider TDC. Distinguishability 0.607 (>0.3), asymmetry 2.55× (≥1.5×) Not in fluorosim codebase — designed & validated by XCath. Merge target: Sprint 2.
4. DeepDRR vs FluoroSim Validation
Analysis only — no code
SSIM=0.964, MAE=9.3%, PSNR=19.01 dB, Pearson=0.981 Beam hardening cancels in DSA subtraction — monoenergetic rendering sufficient for DSA training data generation. External benchmarking by XCath — no code change needed. Finding informs Sprint 2 polyenergetic renderer priority.
5. Misregistration Jitter
Implemented ✓
Controlled mask↔contrast shift: σ_rot=0.05°, σ_trans=0.1 mm. Introduces bone-edge residuals matching real DSA statistics. Implemented in fluorosim: apply_misregistration() — realism.py misregistration_px param — DSASettings / dsa.py
Strategic takeaway: XCath provided clinical validation that turned the simulator into a calibrated training data generator. Items 1–3 are algorithmically proven — merging them into fluorosim is a 2–3 day Sprint 2 task.

## Slide 14
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Sprint 1 — Completed Deliverables
Rendering
Slang GPU Beer-Lambert DRR (512×512, ~25 FPS)
Inline catheter compositing (depth-correct, fused)
Per-segment μ + radius (marker / shaft / tip profile)
Cone-beam magnification (SID/SDD depth scaling)
Batched multi-env DRR (N envs, single Slang dispatch)
Differentiable rendering (6-DOF pose gradients, autodiff)
Detector Realism + DSA
Poisson quantum noise (photon-count model)
Detector PSF convolution (scintillator light spread)
Gamma correction + normalize
Misregistration jitter ✓ implemented (realism.py, dsa.py)
4-step DSA pipeline (mask→contrast→subtract→post)
Temporal bolus dynamics (gamma-variate + Dijkstra arrival map)
Volumetric instrument injection (Warp atomic_max, ~2 ms)
9 vendor C-arm geometry presets
Hagen-Poiseuille / F-8 / Dispersion ⚠ validated, not yet merged
Physics Solver
Cosserat rod XPBD (block-Thomas direct solve)
4 solver backends (block-Thomas, split-Thomas, Jacobi, Cholesky)
Multi-env batched physics (_BatchedWorkspace, flat buffers)
CUDA-graph capture (wp.ScopedCapture + wp.capture_launch)
GPU-side proximal control (push + rotate, CUDA-graph safe)
Floor collision (configurable restitution, Newton parity)
Vessel-mesh SDF containment (wp.mesh_query_point_sign_normal)
AABB broadphase + edge contacts (wp.mesh_query_aabb)
Track-guided insertion (linear insertion axis constraint)
Integration
CT ingestion pipeline (HU→μ + vessel mask + wp.Mesh)
Unified sim loop (physics→render→RL obs, no CPU sync)
Interactive Gradio UI (browser-based, --share public link)
RL training pipeline (RSL-RL PPO, 512 envs, smoke test)
Live catheter bend indicator (vessel collision confirmation)
pip-installable CLI (xcath-fluoro entry point)

## Slide 15
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
Roadmap — Sprint 1 → Sprint 2 → Sprint 3+
TODAY (Sprint 1 — Operational)
GPU Beer-Lambert DRR @25 FPS / 512²
XPBD physics @1,300 Hz / env
Vessel-mesh SDF + AABB collision
DSA pipeline + temporal bolus
9 C-arm vendor presets
State-based PPO (512 envs)
Interactive demo (Gradio UI)
25 FPS end-to-end sim loop
SPRINT 2 (Renderer Scaling + Pixel Obs)
Texture2DArray renderer (>60 Hz @ 512 envs)
Pixel observations for RL (raw fluoroscopy input)
First end-to-end PPO policy (fluoroscopy → action)
Polyenergetic rendering (beam hardening correction)
GPU-side Poisson / PSF pipeline
MAISI synthetic CT (multi-patient training)
Curriculum learning (difficulty progression)
SPRINT 3+ (Clinical AI Pipeline)
2D/3D registration model (end-to-end via autodiff)
Vessel segmentation from fluoroscopy
XCath robot integration (policy → hardware commands)
Holoscan IGX deployment (<10 ms inference)
Multi-patient validation (5+ CTA datasets)
Domain randomization study (sim-to-real gap measurement)
Clinical data paired evaluation
This project is data infrastructure for robotic catheter AI. Sprint 1 built the foundation. Sprint 2 closes the sim-to-real loop. Sprint 3 deploys to a clinical robot.