## Slide 1
X-Ray–Guided Robotic
Catheter Intervention
Simulation Workflow — Release Status & Roadmap
Isaac for Healthcare · NVIDIA Healthcare — Holoscan Team

## Slide 2
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Agenda
• Executive Snapshot — where the X-Ray catheter workflow is today
• Current Status — what's running, with numbers
• This Release — features shipping now (Sprint 1)
• Next Release — Sprint 2 priorities
• Following Releases — Sprint 3 & agentic workflow phases
• Workflow Enhancements — adjacent capabilities on the roadmap
NVIDIA Healthcare — Holoscan Team · 2 / 35

## Slide 3
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCATH Robotics — Partner Requirements
Real-time neurointerventional monitoring system · Jung-eun Park, AI/ML Engineer · March / April 2026
What XCATH Is Building
• Real-time monitoring system for neurointerventional surgery
• → 3D vessel overlay on live fluoroscopy during catheter procedures
• Required AI components:
• 1. Vessel segmentation on intra-op fluoroscopy
• 2. 2D/3D Registration: pre-op CTA ↔ intra-op fluoroscopy
• The Bottleneck:
• Paired training data (CTA + fluoroscopy + GT pose) does NOT
• exist at scale — different modalities, acquisition times, positions
• Why NVIDIA's Simulator:
• Input: CTA volume + vessel mask + pose parameters
• Output: Synthetic fluoroscopy / DSA image + exact GT 3D→2D pose
• → Unlimited paired data for registration & segmentation training
Simulation Methods Validated (March 2026)
• [OK] Method 1: DRR — base fluoroscopy from CTA volume
• [OK] Method 2: Vessel Boost — μ × 8 on vessel-masked voxels
• [OK] Method 3: DSA — mask subtraction + scatter/misregistration
• [OK] Method 5: Bolus Centerline — VMTK + Dijkstra + gamma-variate
•
• Next steps requested from NVIDIA:
• • Synthetic dataset generation at scale
• (CTA + synth DSA + GT pose → train registration)
• • 2D/3D registration model (PoseNet / DiffDRR architecture)
• • Realism evaluation: FID, SSIM, vessel visibility
• • 50-patient internal CTA+DSA paired dataset available
• (cannot be shared; used for validation only)
Source: XCATH Robotics × NVIDIA Technical Collaboration — March 2026 presentation.
NVIDIA Healthcare — Holoscan Team · 3 / 35

## Slide 4
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCATH — April 2026 Progress & Validated Metrics
Weekly Progress 2026-04 W2–W3 · FluoroSim vs DeepDRR · Selective injection · Dispersion correction
Area | March 2026 | April 2026 W1–W3 | Status
DSA rendering | Contrast-only (bone visible) | Mask subtraction + selective injection (F-8) | ✓ DONE
Blood flow model | v=150·(r/r_ref)^0.5, allometric | v=350·(r/2.0)², Hagen-Poiseuille (power=2) | ✓ DONE
Bolus delay match vs real DSA | 5.6 s vs 2.13 s (2.6× off) | 1.90 s vs 2.13 s (89% match) | ✓ DONE
Bolus dispersion | None — all voxels same shape | β_eff = β₀ + k·T + α/r (2.55× asymmetry) | ✓ DONE
Selective injection | 4 roots simultaneous | Feeding Trunk Excision F-8; 43.1% territory | ✓ DONE
FluoroSim vs DeepDRR | Qualitative only | SSIM=0.964, MAE=9.3%, Pearson=0.981 | ✓ DONE
Code quality | Monolithic scripts | Modular + 125 tests + adapter.py + Dockerfile | ✓ DONE
Multi-patient validation | Patient #1 only | 2–3 more patients needed | [PEND] Blocked on data
Remaining Gaps Identified by XCATH
• Beam hardening (monoenergetic): noise CV sim 0.47 vs real 1.46 (3.1×) — requires polyenergetic rendering
• Iodine K-edge (33.2 keV): 70 keV misses 2.5× μ jump → DSA vessel signal weaker than real
• Focal-spot blur: point-source renderer → vessels appear crisper than clinical (mitigation: multi-source render)
• Finer distal cortical branches: limited by CTA annotation density — not a simulator gap
Key finding: monoenergetic rendering (70 keV) is practically sufficient for cerebral DSA (beam hardening cancels in mask subtraction; SSIM=0.964 vs DeepDRR polyenergetic). Source: XCATH Robotics × NVIDIA — April 2026 W2–W3.
NVIDIA Healthcare — Holoscan Team · 4 / 35

## Slide 5
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Executive Snapshot
• X-Ray fluoroscopy simulation pipeline validated end-to-end: physics + Beer-Lambert compositing + Slang GPU fused render
• Fused volume + catheter Beer-Lambert compositing: ~25 FPS single-env; batched multi-env Slang renderer NOW IMPLEMENTED
• All three XPBD rod backends now multi-env: production (PyTorch) + self-contained (Warp) + Newton bridge wrapper
• Self-contained XPBD: batched block-Thomas + GPU root control + CUDA-graph capture + floor restitution + 4 solver backends
• Full detector physics chain: Poisson + scatter + PSF + gamma + misregistration jitter (CPU path; GPU port = Sprint 2)
• Full DSA pipeline (4-step) + vessel boost + gamma-variate bolus dynamics + VMTK/Dijkstra arrival map
• Volumetric instrument injection via Warp atomic-max compositing (~2 ms / 64 nodes / 512³)
• 9 vendor C-arm presets (GE, Siemens, Philips, Ziehm) + state-based RL (PPO, 512 envs)
• E2E validated: catheter traverses 35 mm across cranial anatomy in Slang fused render with correct Beer-Lambert polarity
• Vessel mesh collision: XCathRodSolver ported from Newton xcath branch — SDF BVH + AABB/edge kernels + track-guided insertion
• Critical remaining gap: image-based RL observations + GPU-side detector physics + beam hardening
NVIDIA Healthcare — Holoscan Team · 5 / 35

## Slide 6
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
X-Ray Fluoroscopy Pipeline — At a Glance
Component | Status | Implementation | Multi-Env
Catheter physics solver | ✓ Implemented | Production XPBD Cosserat rod (Warp + Newton bridge) | ✓ Yes (all 3 backends)
DRR volume rendering | ✓ Implemented | Slang DiffDRR (differentiable autodiff) | ✓ Batched (renderDRR_forward_batched)
Catheter Beer-Lambert compositing | ✓ Implemented | Fused GPU ray-march + CPU detector physics path | ✓ Batched (StructuredBuffer slice)
Volumetric instrument injection | ✓ Implemented | Warp atomic-max kernels, ~2 ms / 64 nodes / 512³ | Sprint 2
DSA pipeline (4-step) | ✓ Implemented | DSAPipeline: contrast/mask DRR + scatter + jitter + boost | Sprint 2
Bolus dynamics (temporal DSA) | ✓ Implemented | VMTK centerline + Dijkstra arrival + gamma-variate C(t) | Sprint 2
C-arm geometry + 9 vendor presets | ✓ Implemented | GE, Siemens, Philips, Ziehm classmethod factories | N/A
Detector physics chain | ✓ Implemented | Poisson + scatter + PSF + gamma + misregistration jitter | N/A
RL training pipeline | ✓ Implemented | PPO via RSL-RL, state observations, 512 envs | ✓ Yes
Vessel mesh collision (catheter-in-vessel) | ✓ Implemented | XCathRodSolver: SDF BVH + AABB/edge + track guidance (xcath_rod_solver.py) | Single-env (multi-env = Sprint 2)
Image-based RL observations | ✗ Planned | Sprint 2+ — pixel obs from fluoroscopy frames | —
Beam hardening (polyenergetic) | ✗ Planned | Closes realism gap vs DeepDRR | —
NVIDIA Healthcare — Holoscan Team · 6 / 35

## Slide 7
PART 1
Current Status
What is built, integrated, and measured today.
NVIDIA Healthcare — Holoscan Team · 7 / 35

## Slide 8
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Catheter Physics — Three Solver Backends
Solver | Description | Multi-Env | Key Features
Production XPBD Cosserat rod | Production-grade solver | ✓ Yes (batched) | Mesh BVH collisions, proximal kinematic control, direct solve
Self-contained XPBD solver | Block-Thomas O(n) direct solve | ✓ Yes (1 thread/rod) | Batched kernels, floor restitution, GPU root control, CUDA-graph capture, zero Newton dependency
Newton XPBD bridge | External bridge to Newton's XPBD | ✓ Multi-env (num_envs restriction removed; uses Newton _BatchedRodWorkspace) | Wraps Newton's block-tridiagonal JMJT solver (PR #1981); no CUDA-graph capture
All three expose 3D centerline positions in metres, scaled ×1000 → mm for the compositing pipeline.
NVIDIA Healthcare — Holoscan Team · 8 / 35

## Slide 9
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Self-Contained XPBD — Multi-Env Upgrade
isaaclab_newton/solvers/xpbd_rod_solver.py — feature parity with Newton's xpbd_rod batched path
Batched data + kernels
• _BatchedWorkspace: concatenated GPU buffers for E rods (positions / orientations / velocities / Jacobians / blocks / λ)
• 11 batched kernel variants: predict_pos/rot, integrate_pos/rot, prepare_compliance, update_constraints, compute_jacobians, inv_inertia, assemble_jmjt, block_thomas, compute_corrections
• Block-Thomas direct solve: 1 GPU thread per rod → cost scales with edges_per_rod, not num_envs × edges
• Per-env material parameters: Young's modulus, torsion modulus, gravity, inverse-inertia diag
• Index arrays: rod_offsets / edge_offsets / particle_rod_id / edge_rod_id (built once at construction)
GPU-side control + diagnostics
• apply_proximal_control_gpu(push_v[:E], rotate_v[:E], dt) — single Warp launch, no CPU sync
• set_root_orientation(env_idx, q) — single-thread launch; safe inside CUDA graph
• Floor collision now supports restitution (0 = inelastic, 1 = perfectly elastic)
• step() captures the entire substep loop into a CUDA graph the first call; replays via wp.capture_launch (~zero CPU overhead)
• max_delta_lambda diagnostic written via wp.atomic_max for convergence monitoring across all envs
• Backward-compatible single-env path preserved (~1,300 Hz, 20 segments, A6000)
Smoke-tested: num_envs=8 step + apply_proximal_control_gpu + set_root_orientation all pass; positions tensor returns (num_envs, num_points, 3) when batched, (num_points, 3) when single-env.
NVIDIA Healthcare — Holoscan Team · 9 / 35

## Slide 10
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Fluoroscopy Rendering — Three Compositing Paths
Path | Compositing | Performance
Slang GPU (unified loop) | Fused volume + catheter Beer-Lambert in single GPU ray march | ~25 FPS @ 512×512 (A6000)
CPU Beer-Lambert | Per-segment cylinder chord → attenuation map → I = I_DRR × exp(−atten) + scatter + PSF + Poisson | ~2–5 FPS (NumPy)
Isaac Lab 3D USD quad | DRR backdrop + capsule markers in Omniverse viewport | Real-time (RTX)
Key property: Beer-Lambert is multiplicative — catheter attenuates rather than occludes, with smooth sub-pixel cylinder edges and depth-correct self-crossings.
NVIDIA Healthcare — Holoscan Team · 10 / 35

## Slide 11
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Beer-Lambert Detector Physics Chain (CPU path)
# | Step | Purpose
1 | Attenuation map: t(d) = 2√(r² − d²) per segment | Exact cylinder chord thickness
2 | I_final = I_DRR × exp(−atten_map) | Beer-Lambert transmission
3 | Veiling glare: σ=18 px Gaussian, 3% re-add | X-ray scatter in tissue + housing
4 | Detector PSF: σ=0.7 px Gaussian | CsI scintillator finite resolution
5 | Poisson noise @ 2000 photons/px | Low-dose pulsed fluoroscopy statistics
Per-segment 5-zone profile: tungsten markers (μ=3.0) → nitinol braid (μ=0.8) → transition → soft polymer (μ=0.15) → platinum tip (μ=5.0).
NVIDIA Healthcare — Holoscan Team · 11 / 35

## Slide 12
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
DSA Pipeline & Bolus Dynamics — Implemented
fluorosim/dsa.py + fluorosim/vasculature.py
DSA Pipeline (DSAPipeline.render_dsa_frame)
• Step 1–2: render mask DRR + contrast DRR at same pose
• Step 3: scatter convolution applied to both (Gaussian σ_s)
• Step 4: independent Poisson + Gaussian noise per DRR
• Step 5: misregistration jitter (sub-pixel shift) on mask
• Step 6: subtract diff = contrast − mask
• Step 7: contrast boost (k=20) → gamma (γ=0.8) → normalize
• Plus render_dsa_sequence() for temporal cine output
Bolus Dynamics (vasculature.py)
• extract_centerlines: VMTK marching-cubes + network extraction
• compute_arrival_map: Dijkstra travel-time over centerline graph
• gamma_variate(t, α, β): C(t) = (t/t_peak)^α · exp(α(1−t/t_peak))
• build_contrast_volume: μ(v,t) = μ_tissue + Δμ · C(t − T(v))
• apply_vessel_boost: μ × A=8 on vessel-masked voxels
• Wired into FluoroSimulator.render_cine via volume_callback
• Enables 150-frame @ 5 FPS = 30 s temporal DSA simulation
NVIDIA Healthcare — Holoscan Team · 12 / 35

## Slide 13
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Volumetric Instrument Injection — Implemented
instrument-injection module — max-attenuation compositing on GPU
Compositing Rule
μ_composited(v) = max(μ_anatomy(v), μ_instrument)
• Bone preserved: μ_bone > μ_polymer → catheter behind bone
• Soft tissue replaced: μ_catheter > μ_tissue → catheter visible
• Multi-instrument: densest material wins per voxel
• Implemented as wp.atomic_max — thread-safe parallel compositing
Instruments + Performance
Material | μ (mm⁻¹) | Use
Polymer | 0.03 | Catheter shaft
Nitinol | 0.08 | Guidewire / shaft
Stainless steel | 0.10 | Needle
Platinum | 0.20 | Marker bands
Tungsten | 0.35 | Radiopaque markers
Iodine contrast | 0.05 | DSA contrast agent
Kernels: paint_spheres_kernel + paint_cylinders_kernel (Warp) Performance: ~2 ms / 64 catheter nodes / 512³ volume (vs ~500 ms for the equivalent CPU painting loop)
NVIDIA Healthcare — Holoscan Team · 13 / 35

## Slide 14
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
C-arm Vendor Presets — Implemented
CarmGeometry classmethod factories — fluorosim/config.py
Vendor / Model | SDD (mm) | SID (mm) | Detector | Pixel (mm)
GE OEC 9900 | 1020 | 510 | 1024 × 1024 | 0.194
GE OEC Elite CFD | 1150 | 575 | 1920 × 1920 | 0.154
GE Innova IGS 540 | 1200 | 750 | 2048 × 2048 | 0.200
Siemens Arcadis Avantic | 1000 | 500 | 1024 × 1024 | 0.195
Siemens Cios Alpha | 1100 | 550 | 1536 × 1536 | 0.178
Siemens Artis zee | 1250 | 780 | 2480 × 1920 | 0.154
Philips BV Pulsera | 990 | 495 | 1024 × 1024 | 0.200
Philips Azurion 7 | 1240 | 780 | 2480 × 1920 | 0.154
Ziehm Vision RFD 3D | 1000 | 500 | 1024 × 1024 | 0.194
Usage: geometry = CarmGeometry.philips_azurion_7() → one-line agent-selectable preset
NVIDIA Healthcare — Holoscan Team · 14 / 35

## Slide 15
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
X-Ray Performance Baseline
Metric | Target | Current | Notes
Single-env physics FPS | >1,000 Hz | ~1,300 Hz (20 seg, A6000) | ✓ Achieved
Slang GPU compositing (fused) | <5 ms @ 512² | ~40 ms (~25 FPS) | Single GPU ray march
CPU Beer-Lambert compositing | <2 ms/frame | ~200–500 ms/frame | NumPy; Warp port → 30+ FPS
Multi-env physics (batched XPBD) | >60 Hz @ 512 envs | ✓ Available | Batched block-Thomas + CUDA-graph capture; all 3 backends
Multi-env Slang rendering (batched) | >60 Hz @ 512 envs | ◐ ~25 FPS @ N=1; similar at N≤4 | RWStructuredBuffer path live; Texture2DArray upgrade for N>8 = Sprint 2
NVIDIA Healthcare — Holoscan Team · 15 / 35

## Slide 16
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
RL Training Pipeline (State-Based)
Component | Description
Environment | Multi-env production solver, proximal push/rotate control, distance-to-target reward
RSL-RL wrapper | Standard VecEnv adapter for RSL-RL PPO
PPO config | Tuned hyperparameters for catheter navigation
Training entry | 512 parallel environments, 1500 max iterations
Smoke test | Validates environment without RL dependencies
State-based only today. Pixel/fluoroscopy observations land in Sprint 2+.
NVIDIA Healthcare — Holoscan Team · 16 / 35

## Slide 17
PART 2
This Release
Sprint 1 — features shipping now.
NVIDIA Healthcare — Holoscan Team · 17 / 35

## Slide 18
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
This Release — Completed Deliverables
Across IsaacLab catheter solver + i4h-sensor-simulation-internal fluoro-simulator
Deliverable | Status / Location
Beer-Lambert compositing (physically-correct transmission) | ✓ CPU + Slang GPU paths
Slang GPU fused DRR + catheter single ray march (depth-correct) | ✓ diffdrr_slang.slang
Per-segment attenuation profile (5-zone catheter model) | ✓ Implemented
Cone-beam magnification of projected catheter radius | ✓ Implemented
Detector physics: Poisson + scatter + PSF + gamma | ✓ realism.py apply_realism()
Misregistration jitter (sub-pixel patient motion) | ✓ realism.apply_misregistration
DSA pipeline (4-step: mask + contrast + subtract + post-process) | ✓ dsa.py DSAPipeline
Vessel boost (μ × A=8) on vessel-masked voxels | ✓ vasculature.apply_vessel_boost
VMTK centerline extraction + Dijkstra arrival map | ✓ vasculature.py
Gamma-variate bolus model + per-frame contrast volume | ✓ vasculature.gamma_variate / build_contrast_volume
Per-frame μ update in cine rendering (volume_callback) | ✓ simulator.render_cine
Volumetric instrument injection (max-attenuation, GPU) | ✓ instrument-injection (Warp atomic_max)
9 vendor C-arm presets (GE, Siemens, Philips, Ziehm) | ✓ CarmGeometry classmethods
Differentiable rendering (Slang autodiff, 6-DOF pose gradients) | ✓ renderDRR_backward kernel
Proximal kinematic control API (push / rotate) | ✓ Implemented
Self-contained XPBD: multi-env batched kernels (1 GPU thread / rod) | ✓ xpbd_rod_solver.py _BatchedWorkspace
GPU-side root control: apply_proximal_control_gpu + set_root_orientation | ✓ CUDA-graph capturable, no CPU sync
CUDA-graph capture for the substep loop | ✓ Auto-captured / replayed in step()
Floor collision restitution (0..1) | ✓ Parity with Newton upstream
RL state-based training pipeline (PPO @ 512 envs) | ✓ Implemented
Multi-env Slang fluoroscopy renderer (batched GPU dispatch) | ✓ renderDRR_forward_batched, StructuredBuffer<Pose/CatheterSegment>
Newton XPBD wrapper: multi-env unlocked (num_envs restriction removed) | ✓ newton_xpbd_rod_wrapper.py — uses Newton _BatchedRodWorkspace
E2E workflow validated: catheter motion visible in Beer-Lambert + Slang renders | ✓ 35 mm traversal, correct Beer-Lambert polarity, NiTi μ_profile
XPBDRodSolver: pre/post-constraint hooks (_pre/_post_constraints_hook) | ✓ Extension points added to _substep + _substep_batched
XCathRodSolver: vessel mesh collision (SDF BVH path) | ✓ xcath_rod_solver.py — _project_vessel_containment_kernel (wp.mesh_query_point_sign_normal)
XCathRodSolver: AABB/edge collision path (vertex + segment vs mesh-edge) | ✓ _project_mesh_vertex/edge_collision_kernel_averaged (wp.mesh_query_aabb)
XCathRodSolver: track-guided insertion + configurable collision ordering | ✓ _track_sliding_kernel; pre/post-constraint stage; Gauss-Seidel iterations
E2E vessel collision validation: catheter constrained in synthetic aortic tube | ✓ docs/e2e_vessel/ — tip follows vessel Z-undulation under gravity + push control
NVIDIA Healthcare — Holoscan Team · 18 / 35

## Slide 19
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
This Release — Closed Gaps vs XCATH Requirements
Capability | Before | This Release
Catheter Beer-Lambert compositing | Missing | ✓ Fused GPU + CPU path
Per-segment attenuation profile (5-zone) | Missing | ✓ tungsten / nitinol / polymer / platinum
Detector physics (Poisson + scatter + PSF) | Missing | ✓ realism.py apply_realism()
DSA pipeline (4-step: contrast / mask / subtract / post) | Missing | ✓ dsa.py DSAPipeline
Vessel boost (μ × A=8) | Missing | ✓ vasculature.apply_vessel_boost
Bolus dynamics — gamma-variate C(t) + per-frame μ | Missing | ✓ build_contrast_volume + render_cine
VMTK centerline + Dijkstra arrival map | Missing | ✓ extract_centerlines + compute_arrival_map
Gamma correction (γ=0.8 clinical display TF) | Missing | ✓ In RealismConfig + DSASettings
Physical scatter convolution | Partial (2D veiling only) | ✓ realism.apply_scatter (Gaussian)
Misregistration jitter (DSA mask motion) | Missing | ✓ realism.apply_misregistration
C-arm clinical presets | Partial (docstrings only) | ✓ 9 vendor classmethod factories
Cone-beam magnification | Missing | ✓ Implemented
Per-frame μ update in cine rendering | Missing | ✓ render_cine(volume_callback=…)
Max-attenuation volumetric instrument injection | Planned | ✓ Warp atomic_max kernels
Fused GPU DRR + catheter (single ray march) | N/A | ✓ NEW capability
State-based RL pipeline | Missing | ✓ PPO @ 512 envs
Multi-env XPBD (self-contained solver) | Single env only | ✓ Batched block-Thomas, 1 GPU thread/rod
GPU-side proximal control (no CPU sync) | CPU-bridged via PyTorch | ✓ apply_proximal_control_gpu kernel
CUDA-graph capture of substep loop | Per-step launch overhead | ✓ Auto-captured in step()
Multi-env Slang fluoroscopy renderer | Single-env only | ✓ renderDRR_forward_batched (dispatchThreadID.z)
Newton XPBD wrapper multi-env | Single-env restriction | ✓ num_envs restriction removed; uses _BatchedRodWorkspace
E2E catheter motion in renders | Not validated | ✓ 35 mm traversal, correct polarity, NiTi μ_profile
Vessel mesh collision (catheter-in-vessel containment) | Not implemented | ✓ XCathRodSolver: SDF BVH + AABB/edge + track guidance (xcath_rod_solver.py)
XPBD pre/post-constraint extension hooks | Single _project_predicted_positions hook | ✓ _pre/_post_constraints_hook in _substep + _substep_batched
E2E vessel collision validation | No anatomical constraint | ✓ Catheter tip follows vessel Z-undulation against gravity (docs/e2e_vessel/)
NVIDIA Healthcare — Holoscan Team · 19 / 35

## Slide 20
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
This Release — Genuinely Remaining Items
Items still missing after auditing IsaacLab + i4h-sensor-simulation-internal
Deliverable | Status | Notes
Image-based RL observations (pixel obs) | ✗ Not wired | Catheter env is state-only today
GPU-side detector physics (scatter / PSF / Poisson on Slang path) | ◐ CPU only | Fine for offline data gen; needed for in-loop GPU training
Texture2DArray upgrade for Slang multi-env path | ◐ RWStructuredBuffer only | Needed for cache-efficient rendering at N>8 envs
Beam hardening (polyenergetic correction) | ✗ Not implemented | Monoenergetic only — closes gap vs DeepDRR
Selective injection (hemisphere masking) | ✗ Not implemented | Bilateral CTA → unilateral DSA realism gap
Realism evaluation metrics (FID / SSIM / vessel visibility) | ✗ Not implemented | Needed for agent's iterative refinement loop
3D physics-based scatter (vs 2D Gaussian convolution) | ◐ 2D model only | Gaussian scatter approximation in place
NVIDIA Healthcare — Holoscan Team · 20 / 35

## Slide 21
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Multi-Env Slang Renderer — COMPLETED
diffdrr_slang.slang + diffdrr_slang_renderer.py — batched GPU dispatch now live
Slang shader changes (diffdrr_slang.slang)
• [OK] renderDRR_forward_batched: [CudaKernel] uint3 dispatchThreadID (z = envIdx)
• [OK] StructuredBuffer<Pose> poses — one pose per env; indexed by dispatchThreadID.z
• [OK] StructuredBuffer<CatheterSegment> + StructuredBuffer<int> offsets + counts — concatenated batch
• [OK] catheterAttenuation_slice / rayMarchWithCatheterSlice helpers for per-env buffer slicing
• [OK] Output: flat RWStructuredBuffer<float> at envIdx × H × W + y × W + x
• Known limit: RWStructuredBuffer<float> vs RWTexture2D — texture cache miss at large N; Texture2DArray upgrade = Sprint 2
Python wrapper (diffdrr_slang_renderer.py)
• [OK] SlangDiffDRRRenderer(num_envs=N) — backward-compatible (num_envs=1 unchanged)
• [OK] render_batch(poses) + render_batch_with_catheter(poses, catheters) APIs
• [OK] Lazy persistent GPU buffers: _ensure_batch_buffers() — no realloc when N is stable
• [OK] _upload_poses / _upload_catheters: in-place copy_from_numpy (no new allocation per frame)
• [OK] _readback_batch: to_numpy().view(np.float32) — correct typed readback from RWStructuredBuffer
• [OK] Smoke-tested: 15/15 tests pass across 1→32 envs, with and without catheter, mixed batches
[OK] COMPLETED — batched Slang multi-env rendering is live and smoke-tested. Performance parity with serial path at N≤4; Texture2DArray upgrade improves cache efficiency at N>8 (Sprint 2).
NVIDIA Healthcare — Holoscan Team · 21 / 35

## Slide 22
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
End-to-End Workflow Validation
Physics + Beer-Lambert compositing + Slang GPU fused render — all stages confirmed
Pipeline stages validated
• [OK] Stage 2: Production RodSolver + CPU Beer-Lambert AP view — catheter advances 35 mm across cranial anatomy
• [OK] Stage 3: XPBDRodSolver (self-contained, CUDA graphs) + Beer-Lambert — tip traverses 35 mm in 1 s simulation
• [OK] Stage 4: Production RodSolver dual AP + Lateral views — same catheter trajectory visible in both projections
• [OK] Stage 5: Multi-env XPBD (4 envs, separate solvers) — tip position traces diverge as push velocity differs
• [OK] Stage 6: Pure Slang DRR at 4 C-arm angles (AP / LAO 30° / Lateral / RAO 30°) with real cranial CT
• [OK] Stage 7: Slang GPU fused volume + XPBD catheter — catheter enters right FOV edge, advances 34 mm leftward
Key fixes applied during validation
• [OK] Beer-Lambert polarity: I_final = 1 − (1−I_bg) × t_catheter — catheter now bright white (radio-opaque)
• [OK] μ_profile calibrated: NiTi shaft 0.40 mm⁻¹ tapering to 0.03 mm⁻¹ at soft polymer tip
• [OK] Stage 7 centering: offset computed once at frame 0 — catheter moves through volume, not snaps back
• [OK] Duplicate PUSH_VEL constant found and removed — proximal control was silently overridden to 8 mm/s
• [OK] Catheter enters from right FOV edge at t=0; traverses anatomy leftward at 40 mm/s proximal push
• [OK] 30° Y-rotation applied consistently across Beer-Lambert + Slang stages for matching projection geometry
Output images: source/isaaclab_newton/docs/e2e_output_v2/ (s2–s7 stages, 22 frames total)
NVIDIA Healthcare — Holoscan Team · 22 / 35

## Slide 23
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCathRodSolver — Vessel Mesh Collision COMPLETED
xcath_rod_solver.py — ported from Newton xpbd_rods_solver_integr branch (Przemek Korzeniowski)
Architecture
XCathRodSolver(XPBDRodSolver) — Subclass — no changes to base solver interface
_pre_constraints_hook(ws, dt, dev) — Vessel containment before XPBD solve (optional)
_post_constraints_hook(ws, dt, dev) — Track guidance + vessel containment after XPBD solve
collision_mesh: wp.Mesh — Arbitrary closed triangle mesh (BVH auto-built by Warp)
track_start / track_dir / track_length — Insertion axis — non-tip particles snap to axis
tip_num_edges — Distal free-tip segment count (steerable, unconstrained)
collision_iterations — Gauss-Seidel passes per substep (default 2)
sign_scale / target_phi / max_dist — SDF convention, clearance offset, BVH search radius
Two Collision Paths
• SDF path (default): wp.mesh_query_point_sign_normal
• → BVH signed-distance, ~O(log N) per particle
• → Push particle to target_phi clearance from wall
• → Supports smooth vertex normals (area-weighted)
•
• AABB / edge path (use for tight curvature):
• → _project_mesh_vertex_collision_kernel_averaged
• AABB broadphase, vertex-vs-triangle contacts
• → _project_mesh_edge_collision_kernel_averaged
• Rod-segment vs mesh-edge closest-point contacts
• → Corrections flushed atomically per Gauss-Seidel iter
•
• E2E validation: synthetic aortic tube (13 mm radius,
• Z-undulating path). Tip tracks vessel Z-curve
• against gravity (Δz = +2.7 mm over 40 mm push). ✓
Base class XPBDRodSolver now exposes _pre/_post_constraints_hook in both _substep (single-env) and _substep_batched (multi-env) for future per-env mesh collision at 512+ envs.
NVIDIA Healthcare — Holoscan Team · 23 / 35

## Slide 24
PART 3
Next Release
Sprint 2 — Texture2DArray, multi-env vessel collision, image observations.
NVIDIA Healthcare — Holoscan Team · 24 / 35

## Slide 25
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Next Release — X-Ray Sprint 2 (Weeks 3–4)
Theme: Image observations & GPU detector physics
• [OK] Multi-env Slang renderer COMPLETED — batched renderDRR_forward_batched dispatch is live
• [OK] Vessel mesh collision COMPLETED — XCathRodSolver: SDF BVH + AABB/edge path + track-guided insertion
• Texture2DArray upgrade for Slang path — improves texture cache hit rate at N>8 envs
• Multi-env vessel collision — extend XCathRodSolver to _substep_batched (one mesh per env)
• Image-based RL observations — wire multi-env fluoroscopy frames into RL observation dict
• GPU-side detector physics — port scatter / PSF / Poisson from NumPy realism.py to Slang/Warp
• End-to-end multi-env benchmark: physics + rendering + RL @ 512 envs; target >60 Hz
Status today: all three XPBD backends are multi-env. Batched Slang renderer is live. Vessel mesh collision (single-env) is now implemented via XCathRodSolver. Remaining Sprint 2 items: Texture2DArray, multi-env vessel collision, image-based RL observations, and GPU-side detector physics.
NVIDIA Healthcare — Holoscan Team · 25 / 35

## Slide 26
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Next Release — Phase 1 Fidelity Items (X-Ray)
Remaining simulation-fidelity work after current implementation audit
Effort | Deliverable
✓ DONE | Multi-env / batched Slang rendering — renderDRR_forward_batched + StructuredBuffer batch path
✓ DONE | Vessel mesh collision — XCathRodSolver (SDF BVH + AABB/edge + track-guided insertion, single-env)
~2 days | Texture2DArray upgrade — replace RWStructuredBuffer output with hardware-cached array for N>8 envs
~2 days | Multi-env vessel collision — extend XCathRodSolver._pre/_post hooks to _substep_batched (one mesh per env)
~3 days | Image-based RL observations — pixel obs from fluoroscopy frames into obs dict
~3 days | GPU-side detector physics on Slang path (scatter / PSF / Poisson kernels)
~2 days | Beam hardening (polyenergetic correction)
~1 day | Selective injection (hemisphere masking) on top of bolus pipeline
~2 days | Realism evaluation module (FID, SSIM, vessel visibility metrics)
DSA, vessel boost, bolus dynamics, gamma, scatter, jitter, C-arm presets, and per-frame μ updates are already implemented in i4h-sensor-simulation-internal — the remaining work focuses on multi-env scaling and image-based RL.
NVIDIA Healthcare — Holoscan Team · 26 / 35

## Slide 27
PART 4
Following Releases
Sprint 3 + agentic workflow integration.
NVIDIA Healthcare — Holoscan Team · 27 / 35

## Slide 28
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Sprint 3 — Training Readiness (Weeks 5–6)
X-Ray catheter navigation policy training
• Domain randomization — C-arm angles, attenuation, photon count, scatter parameters
• Gymnasium wrapper — standard RL ecosystem compatibility
• Per-task CUDA-graph variants — separate graphs for sub-batches with mixed materials
• Image-based observations — fluoroscopy frames as RL inputs
• Automated pytest suite — regression coverage for solver + compositing + renderer
NVIDIA Healthcare — Holoscan Team · 28 / 35

## Slide 29
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Agentic Workflow — Phase 2 (Skill Packaging)
Each pipeline stage wrapped as a portable OpenClaw / NemoClaw Skill
Skill | Purpose
patient-digital-twin | CTA → μ volume + vessel mask + centerline + arrival map
catheter-physics-sim | Newton rod solver + compositing config
sensor-sim-xray | DRR / DSA / vessel-boost rendering modes
dataset-creation | Paired HDF5/WebDataset (frames + pose + GT)
reward-function | RL reward configuration (target, contact, dose, progress, success)
policy-training | IL (GR00T-H) → RL (PPO/SAC) → SIL evaluation
evaluation | Success rate, navigation time, contact force, FID, registration accuracy
NVIDIA Healthcare — Holoscan Team · 29 / 35

## Slide 30
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Agentic Workflow — Phase 3 (Agent Integration)
Week | Deliverable
5–6 | Skill discovery & chaining — parse skill definitions, resolve I/O dependencies
6 | Natural language → config mapping — "use Philips Azurion, DSA mode" → YAML overrides
6–7 | Iterative refinement loop — agent runs evaluation, analyzes metrics, proposes changes, re-runs
7 | Slack / IDE integration — agent posts progress, visualizations, and final reports
Outcome: experiment cycle compresses from weeks → hours, with the agent running continuously.
NVIDIA Healthcare — Holoscan Team · 30 / 35

## Slide 31
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Following Releases — Remaining Capability Gaps
Genuinely-missing items after auditing IsaacLab + i4h-sensor-simulation-internal
Missing Feature | Owning Skill | Why It Matters
Texture2DArray for Slang multi-env path | sensor-sim-xray | Cache-efficient rendering at N>8 envs (RWStructuredBuffer path live)
Image-based RL observations | reward-function, policy-training | Image-guided policies (env is state-only today)
GPU-side detector physics on Slang path | sensor-sim-xray | In-loop GPU training without CPU readback
Beam hardening (polyenergetic) | sensor-sim-xray | Closes realism gap vs DeepDRR
Selective injection (hemisphere masking) | patient-digital-twin | Bilateral CTA → unilateral DSA realism
Realism metrics (FID, SSIM, vessel visibility) | evaluation | Quantitative loop for iterative refinement
3D physics-based scatter (vs 2D Gaussian) | sensor-sim-xray | Higher-fidelity scatter halo
DSA, vessel boost, bolus tracking, per-frame μ update, max-attenuation volume compositing, C-arm presets, gamma, scatter convolution, misregistration jitter, multi-env Slang renderer, Newton wrapper multi-env, E2E workflow validation, and vessel mesh collision (XCathRodSolver) — all closed in this release.
NVIDIA Healthcare — Holoscan Team · 31 / 35

## Slide 32
PART 5
Workflow Enhancements
Adjacent capabilities augmenting the X-Ray catheter workflow.
NVIDIA Healthcare — Holoscan Team · 32 / 35

## Slide 33
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Workflow Enhancements
Capabilities that further augment the X-Ray catheter intervention workflow
Capability | Priority | Integration Effort | Why It Matters for X-Ray Catheter Workflow
Texture2DArray upgrade (Slang multi-env) | High | ~2 days — replace RWStructuredBuffer output | Improves texture cache hit rate at N>8; batched path is live at N≤4
Image-based RL observations | High | ~3 days — wire pixels → obs dict | Enables image-guided policies; current env is state-only
Force / Torque sensing | High | Low — data already in collision solver | Safety reward signal; tip-force penalty for vessel perforation
Beam hardening (polyenergetic) | Medium | Moderate | Closes realism gap vs DeepDRR; improves sim-to-real transfer
GPU-side detector physics on Slang path | Medium | ~3 days — Warp/Slang kernels | Avoids CPU readback in the in-loop training pipeline
FID / SSIM / vessel-visibility realism metrics | Medium | ~2 days | Closes the agent's iterative refinement loop
CBCT reconstruction | Low–Medium | Moderate — batched DRR + FDK | Intra-procedural 3D imaging; reuses existing GPU ray-caster
NVIDIA Healthcare — Holoscan Team · 33 / 35

## Slide 34
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Summary
TODAY
• X-Ray fluoroscopy pipeline implemented end-to-end
• Fused GPU Beer-Lambert at ~25 FPS, physics ~1,300 Hz
• DSA + bolus + vessel boost + 9 vendor C-arm presets
• Volumetric instrument injection (atomic-max, ~2 ms)
• State-based PPO @ 512 envs operational
THIS RELEASE
• Full DSA pipeline (4-step) + temporal bolus dynamics
• Detector physics: Poisson + scatter + PSF + gamma + jitter
• Self-contained XPBD: batched + GPU control + CUDA graphs
• Multi-env Slang renderer: renderDRR_forward_batched live
• Newton XPBD wrapper: multi-env unlocked
• E2E validated: 35 mm catheter traversal in Slang renders
• Vessel mesh collision: XCathRodSolver (SDF BVH + AABB/edge + track)
• 21+ XCATH-required capabilities CLOSED
NEXT RELEASE
• Texture2DArray upgrade (N>8 env cache efficiency)
• Multi-env vessel collision (one mesh per env)
• Image-based RL observations (pixel obs)
• GPU-side detector physics on Slang path
• Beam hardening (polyenergetic correction)
FOLLOWING
• Sprint 3 training readiness (DR, Gymnasium, per-task graphs)
• Phase 2 skill packaging (7 OpenClaw skills)
• Phase 3 agent integration (NL → config → eval loop)
• Realism metrics (FID / SSIM / vessel visibility)
• Workflow extensions: F/T, CBCT
NVIDIA Healthcare — Holoscan Team · 34 / 35

## Slide 35
Questions?
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team