## Slide 1
X-Ray–Guided Robotic
Catheter Intervention
Simulation Workflow — Release Status & Roadmap
Isaac for Healthcare · NVIDIA Healthcare — Holoscan Team

## Slide 2
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Architecture Overview
CT ingestion → physics simulation → X-ray render → RL training loop
CT Ingestion
DICOM/NIfTI → HU→μ → vessel seg → centerline → arrival map → SDF → USD
→
Physics Simulation
XPBD Cosserat rod (3 backends: PyTorch prod / self-contained Warp / Newton bridge) · 512 envs · CUDA graphs
→
X-Ray Rendering
Slang DiffDRR fused volume + catheter · Beer-Lambert compositing · DSA pipeline · 9 C-arm presets
→
RL Training
RSL-RL PPO · state observations (Sprint 1) · pixel/fluoro obs (Sprint 2) · domain randomization
Key Data Flows
• CTA volume (μ array, 512³) ─────────────────────────────────────────────→ Slang ray-marcher
• Vessel mesh + SDF ──────────────────────────────────────────────────────→ XCathRodSolver BVH collision
• Rod positions (Warp tensor) ─────────────────────────────────────────────→ Slang catheter compositing
• Fluoroscopy frame (H×W float) ──────────────────────────────────────────→ RL observation dict (Sprint 2)
• Reward signal ───────────────────────────────────────────────────────────→ RSL-RL PPO update
Sprint 1 complete: CT ingestion → physics → X-ray render → state RL. Sprint 2: fluoroscopy pixel obs + GPU detector physics + multi-env vessel collision.
NVIDIA Healthcare — Holoscan Team · 2 / 16

## Slide 3
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
X-Ray Fluoroscopy Pipeline — At a Glance
Component | Status | Implementation | Multi-Env
Catheter physics solver | ✓ Implemented | Production XPBD Cosserat rod (Warp + Newton bridge) | ✓ Yes (all 3 backends)
DRR volume rendering | ✓ Implemented | Slang DiffDRR (differentiable autodiff) | ✓ Batched (renderDRR_forward_batched)
Catheter Beer-Lambert compositing | ✓ Implemented | Fused GPU ray-march + CPU detector physics path | ✓ Batched (StructuredBuffer slice)
Volumetric instrument injection | ✓ Implemented | Warp atomic-max kernels, ~2 ms / 64 nodes / 512³ | Sprint 2
DSA pipeline (4-step) | ✓ Implemented | DSAPipeline: contrast/mask DRR + scatter + jitter + boost | Sprint 2
Bolus dynamics (temporal DSA) | ✓ Implemented | VMTK centerline + Dijkstra arrival + gamma-variate C(t) | Sprint 2
C-arm geometry + 9 vendor presets | ✓ Implemented | GE, Siemens, Philips, Ziehm classmethod factories | N/A
Detector physics chain | ✓ Implemented | Poisson + scatter + PSF + gamma + misregistration jitter | N/A
RL training pipeline | ✓ Implemented | PPO via RSL-RL, state observations, 512 envs | ✓ Yes
Vessel mesh collision (catheter-in-vessel) | ✓ Implemented | XCathRodSolver: SDF BVH + AABB/edge + track guidance (xcath_rod_solver.py) | Single-env (multi-env = Sprint 2)
Image-based RL observations | ✗ Planned | Sprint 2+ — pixel obs from fluoroscopy frames | —
Beam hardening (polyenergetic) | ✗ Planned | Closes realism gap vs DeepDRR | —
NVIDIA Healthcare — Holoscan Team · 3 / 16

## Slide 4
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCATH Robotics — Partner Requirements
Real-time neurointerventional monitoring system · Jung-eun Park, AI/ML Engineer · March / April 2026
What XCATH Is Building
• Real-time monitoring system for neurointerventional surgery
• → 3D vessel overlay on live fluoroscopy during catheter procedures
• Required AI components:
• 1. Vessel segmentation on intra-op fluoroscopy
• 2. 2D/3D Registration: pre-op CTA ↔ intra-op fluoroscopy
• The Bottleneck:
• Paired training data (CTA + fluoroscopy + GT pose) does NOT
• exist at scale — different modalities, acquisition times, positions
• Why NVIDIA's Simulator:
• Input: CTA volume + vessel mask + pose parameters
• Output: Synthetic fluoroscopy / DSA image + exact GT 3D→2D pose
• → Unlimited paired data for registration & segmentation training
Simulation Methods Validated (March 2026)
• [OK] Method 1: DRR — base fluoroscopy from CTA volume
• [OK] Method 2: Vessel Boost — μ × 8 on vessel-masked voxels
• [OK] Method 3: DSA — mask subtraction + scatter/misregistration
• [OK] Method 5: Bolus Centerline — VMTK + Dijkstra + gamma-variate
•
• Next steps requested from NVIDIA:
• • Synthetic dataset generation at scale
• (CTA + synth DSA + GT pose → train registration)
• • 2D/3D registration model (PoseNet / DiffDRR architecture)
• • Realism evaluation: FID, SSIM, vessel visibility
• • 50-patient internal CTA+DSA paired dataset available
• (cannot be shared; used for validation only)
Source: XCATH Robotics × NVIDIA Technical Collaboration — March 2026 presentation.
NVIDIA Healthcare — Holoscan Team · 4 / 16

## Slide 5
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCATH — April 2026 Progress & Validated Metrics
Weekly Progress 2026-04 W2–W3 · FluoroSim vs DeepDRR · Selective injection · Dispersion correction
Area | March 2026 | April 2026 W1–W3 | Status
DSA rendering | Contrast-only (bone visible) | Mask subtraction + selective injection (F-8) | ✓ DONE
Blood flow model | v=150·(r/r_ref)^0.5, allometric | v=350·(r/2.0)², Hagen-Poiseuille (power=2) | ✓ DONE
Bolus delay match vs real DSA | 5.6 s vs 2.13 s (2.6× off) | 1.90 s vs 2.13 s (89% match) | ✓ DONE
Bolus dispersion | None — all voxels same shape | β_eff = β₀ + k·T + α/r (2.55× asymmetry) | ✓ DONE
Selective injection | 4 roots simultaneous | Feeding Trunk Excision F-8; 43.1% territory | ✓ DONE
FluoroSim vs DeepDRR | Qualitative only | SSIM=0.964, MAE=9.3%, Pearson=0.981 | ✓ DONE
Code quality | Monolithic scripts | Modular + 125 tests + adapter.py + Dockerfile | ✓ DONE
Multi-patient validation | Patient #1 only | 2–3 more patients needed | [PEND] Blocked on data
Remaining Gaps Identified by XCATH
• Beam hardening (monoenergetic): noise CV sim 0.47 vs real 1.46 (3.1×) — requires polyenergetic rendering
• Iodine K-edge (33.2 keV): 70 keV misses 2.5× μ jump → DSA vessel signal weaker than real
• Focal-spot blur: point-source renderer → vessels appear crisper than clinical (mitigation: multi-source render)
• Finer distal cortical branches: limited by CTA annotation density — not a simulator gap
Key finding: monoenergetic rendering (70 keV) is practically sufficient for cerebral DSA (beam hardening cancels in mask subtraction; SSIM=0.964 vs DeepDRR polyenergetic). Source: XCATH Robotics × NVIDIA — April 2026 W2–W3.
NVIDIA Healthcare — Holoscan Team · 5 / 16

## Slide 6
PART 1
Current Status
What is built, integrated, and measured today.
NVIDIA Healthcare — Holoscan Team · 6 / 16

## Slide 7
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
X-Ray Performance Baseline
Metric | Target | Current | Notes
Single-env physics FPS | >1,000 Hz | ~1,300 Hz (20 seg, A6000) | ✓ Achieved
Slang GPU compositing (fused) | <5 ms @ 512² | ~40 ms (~25 FPS) | Single GPU ray march
CPU Beer-Lambert compositing | <2 ms/frame | ~200–500 ms/frame | NumPy; Warp port → 30+ FPS
Multi-env physics (batched XPBD) | >60 Hz @ 512 envs | ✓ Available | Batched block-Thomas + CUDA-graph capture; all 3 backends
Multi-env Slang rendering (batched) | >60 Hz @ 512 envs | ◐ ~25 FPS @ N=1; similar at N≤4 | RWStructuredBuffer path live; Texture2DArray upgrade for N>8 = Sprint 2
NVIDIA Healthcare — Holoscan Team · 7 / 16

## Slide 8
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
RL Training Pipeline (State-Based)
Component | Description
Environment | Multi-env production solver, proximal push/rotate control, distance-to-target reward
RSL-RL wrapper | Standard VecEnv adapter for RSL-RL PPO
PPO config | Tuned hyperparameters for catheter navigation
Training entry | 512 parallel environments, 1500 max iterations
Smoke test | Validates environment without RL dependencies
State-based only today. Pixel/fluoroscopy observations land in Sprint 2+.
NVIDIA Healthcare — Holoscan Team · 8 / 16

## Slide 9
PART 2
This Release
Sprint 1 — features shipping now.
NVIDIA Healthcare — Holoscan Team · 9 / 16

## Slide 10
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
This Release — Completed Deliverables
Across IsaacLab catheter solver + i4h-sensor-simulation-internal fluoro-simulator
Deliverable | Status / Location
Beer-Lambert compositing (physically-correct transmission) | ✓ CPU + Slang GPU paths
Slang GPU fused DRR + catheter single ray march (depth-correct) | ✓ diffdrr_slang.slang
Per-segment attenuation profile (5-zone catheter model) | ✓ Implemented
Cone-beam magnification of projected catheter radius | ✓ Implemented
Detector physics: Poisson + scatter + PSF + gamma | ✓ realism.py apply_realism()
Misregistration jitter (sub-pixel patient motion) | ✓ realism.apply_misregistration
DSA pipeline (4-step: mask + contrast + subtract + post-process) | ✓ dsa.py DSAPipeline
Vessel boost (μ × A=8) on vessel-masked voxels | ✓ vasculature.apply_vessel_boost
VMTK centerline extraction + Dijkstra arrival map | ✓ vasculature.py
Gamma-variate bolus model + per-frame contrast volume | ✓ vasculature.gamma_variate / build_contrast_volume
Per-frame μ update in cine rendering (volume_callback) | ✓ simulator.render_cine
Volumetric instrument injection (max-attenuation, GPU) | ✓ instrument-injection (Warp atomic_max)
9 vendor C-arm presets (GE, Siemens, Philips, Ziehm) | ✓ CarmGeometry classmethods
Differentiable rendering (Slang autodiff, 6-DOF pose gradients) | ✓ renderDRR_backward kernel
Proximal kinematic control API (push / rotate) | ✓ Implemented
Self-contained XPBD: multi-env batched kernels (1 GPU thread / rod) | ✓ xpbd_rod_solver.py _BatchedWorkspace
GPU-side root control: apply_proximal_control_gpu + set_root_orientation | ✓ CUDA-graph capturable, no CPU sync
CUDA-graph capture for the substep loop | ✓ Auto-captured / replayed in step()
Floor collision restitution (0..1) | ✓ Parity with Newton upstream
RL state-based training pipeline (PPO @ 512 envs) | ✓ Implemented
Multi-env Slang fluoroscopy renderer (batched GPU dispatch) | ✓ renderDRR_forward_batched, StructuredBuffer<Pose/CatheterSegment>
Newton XPBD wrapper: multi-env unlocked (num_envs restriction removed) | ✓ newton_xpbd_rod_wrapper.py — uses Newton _BatchedRodWorkspace
E2E workflow validated: catheter motion visible in Beer-Lambert + Slang renders | ✓ 35 mm traversal, correct Beer-Lambert polarity, NiTi μ_profile
XPBDRodSolver: pre/post-constraint hooks (_pre/_post_constraints_hook) | ✓ Extension points added to _substep + _substep_batched
XCathRodSolver: vessel mesh collision (SDF BVH path) | ✓ xcath_rod_solver.py — _project_vessel_containment_kernel (wp.mesh_query_point_sign_normal)
XCathRodSolver: AABB/edge collision path (vertex + segment vs mesh-edge) | ✓ _project_mesh_vertex/edge_collision_kernel_averaged (wp.mesh_query_aabb)
XCathRodSolver: track-guided insertion + configurable collision ordering | ✓ _track_sliding_kernel; pre/post-constraint stage; Gauss-Seidel iterations
E2E vessel collision validation: catheter constrained in synthetic aortic tube | ✓ docs/e2e_vessel/ — tip follows vessel Z-undulation under gravity + push control
NVIDIA Healthcare — Holoscan Team · 10 / 16

## Slide 11
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
This Release — Closed Gaps vs XCATH Requirements
Capability | Before | This Release
Catheter Beer-Lambert compositing | Missing | ✓ Fused GPU + CPU path
Per-segment attenuation profile (5-zone) | Missing | ✓ tungsten / nitinol / polymer / platinum
Detector physics (Poisson + scatter + PSF) | Missing | ✓ realism.py apply_realism()
DSA pipeline (4-step: contrast / mask / subtract / post) | Missing | ✓ dsa.py DSAPipeline
Vessel boost (μ × A=8) | Missing | ✓ vasculature.apply_vessel_boost
Bolus dynamics — gamma-variate C(t) + per-frame μ | Missing | ✓ build_contrast_volume + render_cine
VMTK centerline + Dijkstra arrival map | Missing | ✓ extract_centerlines + compute_arrival_map
Gamma correction (γ=0.8 clinical display TF) | Missing | ✓ In RealismConfig + DSASettings
Physical scatter convolution | Partial (2D veiling only) | ✓ realism.apply_scatter (Gaussian)
Misregistration jitter (DSA mask motion) | Missing | ✓ realism.apply_misregistration
C-arm clinical presets | Partial (docstrings only) | ✓ 9 vendor classmethod factories
Cone-beam magnification | Missing | ✓ Implemented
Per-frame μ update in cine rendering | Missing | ✓ render_cine(volume_callback=…)
Max-attenuation volumetric instrument injection | Planned | ✓ Warp atomic_max kernels
Fused GPU DRR + catheter (single ray march) | N/A | ✓ NEW capability
State-based RL pipeline | Missing | ✓ PPO @ 512 envs
Multi-env XPBD (self-contained solver) | Single env only | ✓ Batched block-Thomas, 1 GPU thread/rod
GPU-side proximal control (no CPU sync) | CPU-bridged via PyTorch | ✓ apply_proximal_control_gpu kernel
CUDA-graph capture of substep loop | Per-step launch overhead | ✓ Auto-captured in step()
Multi-env Slang fluoroscopy renderer | Single-env only | ✓ renderDRR_forward_batched (dispatchThreadID.z)
Newton XPBD wrapper multi-env | Single-env restriction | ✓ num_envs restriction removed; uses _BatchedRodWorkspace
E2E catheter motion in renders | Not validated | ✓ 35 mm traversal, correct polarity, NiTi μ_profile
Vessel mesh collision (catheter-in-vessel containment) | Not implemented | ✓ XCathRodSolver: SDF BVH + AABB/edge + track guidance (xcath_rod_solver.py)
XPBD pre/post-constraint extension hooks | Single _project_predicted_positions hook | ✓ _pre/_post_constraints_hook in _substep + _substep_batched
E2E vessel collision validation | No anatomical constraint | ✓ Catheter tip follows vessel Z-undulation against gravity (docs/e2e_vessel/)
NVIDIA Healthcare — Holoscan Team · 11 / 16

## Slide 12
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
XCathRodSolver — Vessel Mesh Collision COMPLETED
xcath_rod_solver.py — ported from Newton xpbd_rods_solver_integr branch (Przemek Korzeniowski)
Architecture
XCathRodSolver(XPBDRodSolver) — Subclass — no changes to base solver interface
_pre_constraints_hook(ws, dt, dev) — Vessel containment before XPBD solve (optional)
_post_constraints_hook(ws, dt, dev) — Track guidance + vessel containment after XPBD solve
collision_mesh: wp.Mesh — Arbitrary closed triangle mesh (BVH auto-built by Warp)
track_start / track_dir / track_length — Insertion axis — non-tip particles snap to axis
tip_num_edges — Distal free-tip segment count (steerable, unconstrained)
collision_iterations — Gauss-Seidel passes per substep (default 2)
sign_scale / target_phi / max_dist — SDF convention, clearance offset, BVH search radius
Two Collision Paths
• SDF path (default): wp.mesh_query_point_sign_normal
• → BVH signed-distance, ~O(log N) per particle
• → Push particle to target_phi clearance from wall
• → Supports smooth vertex normals (area-weighted)
•
• AABB / edge path (use for tight curvature):
• → _project_mesh_vertex_collision_kernel_averaged
• AABB broadphase, vertex-vs-triangle contacts
• → _project_mesh_edge_collision_kernel_averaged
• Rod-segment vs mesh-edge closest-point contacts
• → Corrections flushed atomically per Gauss-Seidel iter
•
• E2E validation: synthetic aortic tube (13 mm radius,
• Z-undulating path). Tip tracks vessel Z-curve
• against gravity (Δz = +2.7 mm over 40 mm push). ✓
Base class XPBDRodSolver now exposes _pre/_post_constraints_hook in both _substep (single-env) and _substep_batched (multi-env) for future per-env mesh collision at 512+ envs.
NVIDIA Healthcare — Holoscan Team · 12 / 16

## Slide 13
PART 3
Next Release
Sprint 2 — Texture2DArray, multi-env vessel collision, image observations.
NVIDIA Healthcare — Holoscan Team · 13 / 16

## Slide 14
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Next Release — X-Ray Sprint 2 (Weeks 3–4)
Theme: Image observations & GPU detector physics
• [OK] Multi-env Slang renderer COMPLETED — batched renderDRR_forward_batched dispatch is live
• [OK] Vessel mesh collision COMPLETED — XCathRodSolver: SDF BVH + AABB/edge path + track-guided insertion
• Texture2DArray upgrade for Slang path — improves texture cache hit rate at N>8 envs
• Multi-env vessel collision — extend XCathRodSolver to _substep_batched (one mesh per env)
• Image-based RL observations — wire multi-env fluoroscopy frames into RL observation dict
• GPU-side detector physics — port scatter / PSF / Poisson from NumPy realism.py to Slang/Warp
• End-to-end multi-env benchmark: physics + rendering + RL @ 512 envs; target >60 Hz
Status today: all three XPBD backends are multi-env. Batched Slang renderer is live. Vessel mesh collision (single-env) is now implemented via XCathRodSolver. Remaining Sprint 2 items: Texture2DArray, multi-env vessel collision, image-based RL observations, and GPU-side detector physics.
NVIDIA Healthcare — Holoscan Team · 14 / 16

## Slide 15
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team
Summary
TODAY
• X-Ray fluoroscopy pipeline implemented end-to-end
• Fused GPU Beer-Lambert at ~25 FPS, physics ~1,300 Hz
• DSA + bolus + vessel boost + 9 vendor C-arm presets
• Volumetric instrument injection (atomic-max, ~2 ms)
• State-based PPO @ 512 envs operational
THIS RELEASE
• Full DSA pipeline (4-step) + temporal bolus dynamics
• Detector physics: Poisson + scatter + PSF + gamma + jitter
• Self-contained XPBD: batched + GPU control + CUDA graphs
• Multi-env Slang renderer: renderDRR_forward_batched live
• Newton XPBD wrapper: multi-env unlocked
• E2E validated: 35 mm catheter traversal in Slang renders
• Vessel mesh collision: XCathRodSolver (SDF BVH + AABB/edge + track)
• 21+ XCATH-required capabilities CLOSED
NEXT RELEASE
• Texture2DArray upgrade (N>8 env cache efficiency)
• Multi-env vessel collision (one mesh per env)
• Image-based RL observations (pixel obs)
• GPU-side detector physics on Slang path
• Beam hardening (polyenergetic correction)
FOLLOWING
• Sprint 3 training readiness (DR, Gymnasium, per-task graphs)
• Phase 2 skill packaging (7 OpenClaw skills)
• Phase 3 agent integration (NL → config → eval loop)
• Realism metrics (FID / SSIM / vessel visibility)
• Workflow extensions: F/T, CBCT
NVIDIA Healthcare — Holoscan Team · 15 / 16

## Slide 16
Questions?
X-Ray–Guided Robotic Catheter Intervention — Isaac for Healthcare
NVIDIA Healthcare — Holoscan Team